## Slide 1: Lego case assignment
System overview
Bulk to conveyor
Single line bricks
Size sorting
Weighting and image collection
Data Analysis => Brick id
Sorting to sets

## Slide 2
Bulk to conveyor
Single line bricks
This is done to track the single brick
The PLC should be the master which triggers the cameras
The vision system then simply reports to the PLC what the classification is
The PLC will also be in charge of updating the database and the running sets as described later on.
PLC
Vision system
Pick and place
Database

## Slide 3
Size sorting
Weighting and image collection
Data Analysis => Brick id
If the bricks should be size and/or color sorted into a number of categories
This will make it simpler to categorize with a series of different CNN each specializing in that size/color
The shape of the brick could be added with a 2D laser line on the belt.
As added info each brick could also be weighed.
It could be necessary to get a second images after a flipping of the brick.
If neither images are conclusive the brick would end up in the rerun bucket.
All images should be saved with prod_id possible in the cloud or on a sperate NAS

## Slide 4
Sorting to sets
Set_id =251
Set_id =211
Set_id =251
Set_id =2
Every station has its own robot/bucket and its own running set that it is working on
If a brick comes by that is not yet in the set but is needed the bucket will turn
The running set will then be updated.
Once a set is complete a picture will be taken of the set. This could work as a validation.
A complete set will then be packed and a new set will be started at the station.
At the end all the bricks which does not fit a running set will end up.
There should be at least twice as many stations as different sets if we expect all to be sorted.
Set_id =42
Rerun/
man. sort